## Slide 1
dw/dsurf on the JWST OTE deck: what each option does to one segment's column
jwst_ote_designc.in (Luis's zoom deck), model 512, 63-ray grid, stop at the FSM (element 25), wavefront read at the ExitPupil Return (27); Seg2 (element 5) poked alone in radius (Kr) and conic (Kc) through run_sensitivities, centre field
DRAFT 2026-09-09. Every option shown is a run_sensitivities option since this date ('orient', 'sign', 'opd_ref', and 'elts' now reach the dwdsurf channel). Numbers: dW/dp per unit parameter, mm of OPD per mm (Kr) / per unit (Kc), centre field, single configuration.

## Slide 2
The OPD reference decides what the unpoked segments read
mean reference: one constant on the other 17; chief reference: exactly zero
Kr and Kc columns of Seg2 under opd_ref = mean (left) and chief (right): the 17 unpoked segments carry a flat offset on the left (the colour scale's top) and exactly zero on the right.
Offset on the unpoked segments under mean = -(N_k/N) x mean(poked response): Kr 4.40e-4, Kc 1.66e-2 per unit parameter (5.4% / 4.5% of the poked segment's rms), equal on all 17 to 6e-16; the mean and chief columns differ by that one constant everywhere (1.4e-12 relative). orient xy, sign opl, surf_remove_ptt off; MATLAB jet colormap, autoscaled colour limits, as in Luis's plots.

## Slide 3
Why: a column is a difference of two referenced maps
poking one segment moves the aperture-mean reference; the chief ray's does not move unless its own segment is poked
Engine OPD
path length minus a reference: whole-aperture mean (default) or the chief ray's own path (macos.opd_ref)
Under mean
the poked segment shifts the mean by (N_k/N) x its mean response; every ray inherits the shift as a piston
Under chief
the reference is one ray; on this deck it passes through the virtual centre segment (element 4), so every REAL segment's poke leaves it alone and the other segments read 0
The one gap
a deck whose chief ray sits on a real segment (e5hex1: the centre one) moves the reference when that segment is poked; the others then read -m(chief), 5% of that segment's rms for Kr. A fixed nominal reference length (engine OPDRefRayLen branch, one api wrapper) localises every column
Gates: tOpdRef/test_driver_single_segment_poke_is_local_under_chief (e5hex1, driver path; fails on the previous code) and tRunSensitivities/test_dwdsurf_channel_honours_elts_orient_and_opd_ref. The default stays 'mean' until the fixed-length reference lands: no committed baseline moves.

## Slide 4
The other options do not remove the leak; they relabel it
PTT removal fits the whole column, orientation transposes, sign negates
The same Kr column with PTT removal (top row: mean and chief become identical, and a tilt now runs across all 18 segments), raw orientation (bottom left: the same rays with index 1 along global X, the spiders rotate) and the wavefront sign (bottom right: negated).
surf_remove_ptt fits global piston/tip/tilt to the whole column: the poked segment biases the fit, so the 17 unpoked segments trade a 4.4e-4 flat offset for a tilt of 7.0e-4 rms, and the reference choice no longer matters. Orientation check: Seg2 sits at (X, Y) = (-1137, +657) mm and its footprint appears at (+10, -6.5) px from the pupil centre in the xy map, i.e. columns run along xGrid = -X and rows along yGrid = -Y (the deck's source frame; magnitudes match the exit-pupil scale). 'xy' fixes the transpose, not the sign of each axis.

## Slide 5
What to run
the options, where they live, and the recommended call on a segmented deck
option | values | now taken by | recommended (segmented)
opd_ref | mean (default), chief | all 8 dw_d* drivers, the core, run_sensitivities | chief
orient | raw (default), xy | same | xy for display
sign | opl (default), wavefront | same | as the consumer needs
elts | [] (all eligible), ids | run_sensitivities -> all four channels (dwdsurf was dropped) | the segments of interest
surf_remove_ptt / remove_ptt | false (default), true | dwdsurf driver + runner | false (not a substitute for the reference)
run_sensitivities(RX, ..., 'channels', "dwdsurf", 'elts', 5, 'orient', 'xy', 'opd_ref', 'chief'). The reference is re-applied after every Rx reload (a load resets it). Open for Dave: the fixed nominal reference and the default flip (PLAN 0.x).