## Slide 1
A VSWIR Dyson Imaging Spectrometer, Designed From the Spec
An EMIT-class push-broom spectrometer (F/1.8, 3000 × 500 pixels at 18 µm, 380–2500 nm) designed with MACOS from the public specification alone, scored on smile, keystone and the response functions, and checked by physical-optics propagation.
D. C. Redding, with Claude Code.
October 2026. Working record; no proprietary prescription is used.
DRAFT — in progress. Every number is from a committed, parameterized runner (mmacos, dyson5_run); records and figures are the runner's own output.

## Slide 2
Contents
The target, the forms, the design ladder, the evidence
• 3 The target and how it is scored
• 4 The Dyson as traced by the engine
• 5 The Offner as traced by the engine
• 6 The concentric Dyson and its scaling law
• 7 The exact chain and the engine agree
• 8 The seed, scored
• 9 The departure ladder
• 10 The departure ladder, by the numbers
• 11 What each departure buys
• 12 Next: the compact variant
• 13 Run it yourself
• 14 Backup

## Slide 3
The target and how it is scored
Joe's specification, EMIT-class; the metrics stated once, here
item | value
F-number (air-equivalent, image space) | 1.8
focal plane | 3000 spatial × 500 spectral pixels, 18 µm
slit | 54 mm; spectral height 9 mm
band | 380–2500 nm, 4.24 nm per pixel
smile, keystone | < 0.1 pixel
SRF FWHM | < 1.5–2.0 pixels
CRF FWHM | < 1.5 pixels
radiometric chain | throughput, grating efficiency, QE, slit loss vs wavelength
• Smile: centroid drift along the slit at fixed wavelength; keystone: drift across wavelength at fixed slit position; both in pixels from ray centroids.
• SRF, CRF: slit ⊗ line-spread function ⊗ pixel ⊗ Airy, FWHM in pixels (Mouroulis & Green 2018 definitions); the Airy diameter at 2500 nm is 11 µm, under the 18 µm pixel, so the incoherent chain is valid.
• Design rules adopted from the literature: distortion to ~1 % of a pixel at design, > 75 % of the energy in one pixel, degraded spots accepted for uniformity, the grating is the stop.
• Realism (Jim): as-built SRF is 2.5–3 pixels, slits are 2 pixels wide, the systems are photon-limited; smile and keystone drive the design.
The 54 mm slit is 2.3× EMIT's; Table 3 of the review places this spec in the ALIS class (3200 spatial pixels, 380–2500 nm). Public comparison point: Carbon-I (arXiv:2505.22545), F/2.2, 2040–2380 nm.

## Slide 4
The Dyson as traced by the engine
Step R3 of the ladder: silica block, air gap, concave grating at the stop; rays from the slit return dispersed to the focal plane on the block's face
• The prescription: challenges/dyson5/dyson5_s3_r3.in, seven elements; the block's spherical face (E2), the grating (E3, radius 0.71 m at the Dyson condition for a 220 mm block), and the focal plane on the flat face. Bodies, rays and labels are read back from the engine.
• The slit sits on the block's flat face, so the glass is the source medium and only the spherical face is a refracting element; the dispersion is the fan in the right-hand (Y-Z) view returning to the face.
Left: the traced bundle and the solid bodies in 3-D. Right: the dispersion plane (Y-Z). Positions in metres, global frame.

## Slide 5
The Offner as traced by the engine
The all-reflective twin: concave mirror, convex grating at the common centre, concave mirror; all in air
• The prescription: challenges/dyson5/dyson5_s1_offner.in, five elements; the concave mirror (E1, used twice), the convex grating (E2) at the stop, the focal plane at the slit's conjugate.
• Why it is in the deck: it is where the physical-optics twin is validated (order 0: pupil OPD 8e-11 m, 94 % of the energy in one pixel), and it is the trade's reference form.
Left: the traced bundle and the solid bodies in 3-D. Right: the dispersion plane (Y-Z). Positions in metres, global frame.

## Slide 6
The concentric Dyson and its scaling law
The classical condition verified by exact trace; at this slit the concentric block needs r ≥ 213 mm
• The Dyson condition R_g = n·r / (n − 1) is the blur minimum by exact 3-D trace: 0.67 µm at the condition against 4–5 µm at ±5 %, image at −h, residual fifth order (h⁴·¹⁷, r⁻³·¹⁹).
• The scaling answer, before any element was added: a single concentric block meets a quarter-pixel corner blur only at r ≥ 213 mm, about twice flight scale, which is why the flight forms add an asphere, a meniscus or an air gap.
Rms blur at the slit corner (h = 28.2 mm) of a concentric silica Dyson at F/1.8 versus block radius, exact trace at order 0: blur ∝ r⁻³·¹⁹; the quarter-pixel budget is met at r = 213 mm (grating radius 687 mm).

## Slide 7
The exact chain and the engine agree
Every engine ray re-traced by the chain from the engine's own launch directions lands within 1e-9 m
• The check: the engine's chief ray and every ray of its grid are re-traced through the chain's surfaces from the engine's launch directions; agreement is per ray, every surface, 1e-9 m; the dispersed band spans the focal plane to 1 %.
• With the aspheric block face (ladder step R2): agreement 1e-12 m per ray; a sphere-only chain misses by 0.26 mm, so the check is not vacuous.
• The physical-optics twin: a far-field terminal on a reference sphere upstream of the focal plane, re-posed per slit position and wavelength; on the Offner at order 0 the pupil OPD is 8e-11 m and the Airy spot puts 94 % of its energy in one 18 µm pixel.
• What the checks found in the engine, now fixed (details in Backup): glass names were ignored at load; propagation inside glass used the vacuum wavelength; the grating groove period was held constant along the curved surface instead of along the chord; the grating's path-length jump had the matching defect. Each has a regression test written from the physics, not from the engine.
Regression tests: tSpectrometerRx (3), tGratingOpl (2), tGratingImmersed (4), tGlassDispersion (3), tPropMedium (3); mmacos fast suite 501 pass, 0 fail (2026-10-01).

## Slide 8
The seed, scored
The concentric seed at a 220 mm block meets smile; keystone and the corner blur are the work
• Smile is met at the seed (below 0.01 pixel on both forms); the field-angle map is linear along the slit as designed.
• These maps predate the grating fixes of 2026-10-01: the SRF ramp with wavelength is the groove-period defect, not the design; the re-scored maps replace this figure.
Scorer maps for the two seeds at 220 mm (rows: Dyson, Offner): field-angle map, smile (pixels), SRF FWHM (pixels), ensquared energy in one pixel, versus slit position and wavelength.

## Slide 9
The departure ladder
Each step solved on the exact chain with pixel-unit smile and keystone in the merit from the first pass, then emitted and scored in the engine
Engine-scored maxima per ladder step at the seed's 220 mm block (left: smile, keystone, CRF FWHM in pixels; right: minimum ensquared energy in one pixel against the 0.75 design rule).

## Slide 10
The departure ladder, by the numbers
Keystone falls nine-fold at fixed scale; smile and SRF stay at their floors
step | what moves | keystone (px) | smile (px) | CRF FWHM (px) | ensquared, 1 px
R0 | concentric seed | 0.095 | 0.006 | 2.28 | 0.44
R1 | grating-radius factor, face offset | 0.038 | 0.003 | 2.10 | 0.48
R2 | + conic and h⁴, h⁶ terms on the block face | 0.037 | 0.004 | 2.13 | 0.47
R3 | + block centre 0.86 mm off the grating's, along the dispersion | 0.011 | 0.008 | 2.10 | 0.48
SRF FWHM is 2.02 px on every step: the floor set by the 2-pixel slit. Records dyson5_s3.txt; the free-radius variant in dyson5_s3free.txt.

## Slide 11
What each departure buys
De-concentring the block solves the distortion; the face asphere is inert; the blur is bought only by size or by the compact form
• Keystone: 0.095 → 0.011 pixels at fixed scale, nine times inside the 0.1-pixel specification and at the literature's 1 % design rule; smile stays below 0.01 pixel throughout.
• The block-face asphere does nothing here: step R2 converges to 10 nm sags, and a one-dimensional scan about R1 is a steep bowl centred at zero. An axisymmetric figure acts on every field point alike and cannot cancel a residual that grows as h⁴ along the slit.
• The blur does not move on any step, and the reason is on record: the dispersed image sits 12 mm from the order-0 image, so the slit corner's effective field height is about 32 mm, and the h⁴/r³ law predicts the measured 0.4 px rms.
• Two routes buy it: size alone (the free-radius variant reaches 0.74 ensquared at a 341 mm block) or the literature's compact variant, a separate mirror and a meniscus — the next step.
The free-radius ladder: ensquared energy reaches the 0.75 rule only as the block grows to 341 mm.

## Slide 12
Next: the compact variant
Step R4 under the identical operands and scorer, so the trade is one table
• R4: the compact Dyson of the review — a separate mirror and a meniscus — solved on the same chain with the same smile and keystone operands, emitted and engine-scored like every other step.
• One trade table: R3 (de-concentred block at 220 mm), the free-radius block (341 mm), and R4, on keystone, smile, CRF, SRF, ensquared energy, length, footprint, element count and glass volume.
• Then the physical-optics twin on the chosen design: PSF centroids against ray centroids, SRF and CRF from the propagated PSF, the slit-width diffraction loss against the sinc² closed form.
• Then the native multi-wavelength optimizer with the same operands, to confirm the chain's optimum from the engine side.
Across a grating the wavefront is defined only modulo λ (the groove staircase); every OPD comparison in the twin is made in phase or on the complex field, never as unwrapped lengths.

## Slide 13
Run it yourself
One parameter file, one runner, every stage through it
run('<path>/mmacos/mmacos_setup.m');
addpath('<path>/mmacos/challenges/dyson5');
OUT = dyson5_run(); % stage s0: the scaling law (engine-free)
OUT = dyson5_run(struct('stages', {{'s1','s2','s3'}})); % emit, score, ladder
• Knobs live in dyson5_params.m (F-number, pixel, band, slit, block radius, ladder options); every record in this deck is a stage output under challenges/dyson5/.
• Engine checks: ./run_mmacos_tests.sh tSpectrometerRx and the four grating / glass / propagation classes, all in the fast suite.

## Slide 14
Backup
Diagnostics, the engine findings, and the conventions behind the main path.

## Slide 15
Backup: four engine findings, each with a regression test
Found by the challenge's checks on 2026-09-30 and 10-01, fixed in the engine the same day
finding | symptom | fix | test
glass names ignored at load | a GlassElt= Silica element traced as air in every binding | the glass catalog is blanked once at allocation, not on every load | tGlassDispersion (3)
vacuum wavelength inside glass | a propagation leg in a medium ran at the wrong Fresnel number by n | every kernel takes λ/n of the leg's medium | tPropMedium (3): z in n ≡ z/n in vacuum
groove period along the surface | 2.8 / 3.3 px rms spectral blur at 2500 nm (Offner / Dyson) | the local grating vector is the un-normalised projection of the ruling direction (chord-ruled) | tGratingImmersed (4), test_grating_chord
grating path-length jump | 4 waves rms of pupil OPD where the rays converged to 0.05 µm | the jump is the groove count from the vertex along the ruling direction | tGratingOpl (2)
Flat gratings are unchanged by the last two. A fifth item, a short AsphCoef= line killing the host process, now pads with zero and warns (tRxShortAsph).

## Slide 16
Backup: records and tools behind each slide
Every number traces to a runner stage and its record file
slide | runner stage | record | tool
scaling law | s0 (engine-free) | dyson5_s0_scaling.txt | design/src/dyson_layout.m, dyson_scaling.m
as traced (both forms) | dyson5_view_figs.m | _view3d.png, _viewyz.png | macos.view_rx on the deck
seed scored | s1 emit, s2 score | dyson5_s1.txt, dyson5_s2.txt, dyson5_s2_maps.png | spectrometer_geom.m, spectrometer_rx.m, spectrometer_score.m
chain vs engine | gate | tests/tSpectrometerRx.m | per-ray re-trace, 1e-9 m
propagation twin | s2w (opt-in, model 512) | dyson5_s2w.txt | spectrometer_wave.m
departure ladder | s3, s3free | dyson5_s3.txt, dyson5_s3free.txt, dyson5_s3*_ladder.png | dyson_ladder.m
Conventions behind the scaling law: block index n(silica, 1 µm) = 1.450417; in-glass marginal half-angle u = asin(1 / 2nF); field height h from the Dyson axis on the flat face; the slit corner is h = hypot(27 mm, 8 mm).

## Slide 17
Backup: conventions pinned on the way
Engine facts the chain depends on, stated once
• ChfRayPos is where rays start and must lie before the first surface; at load the engine folds zSource in once, after which it is the physical source.
• macos.stop aims immediately and its first pass is one step short on this deck (3.6 mrad): declare the stop first, then write the exact chief ray.
• A Return coincident with the focal plane drops the rays; use a Reference upstream.
• An immersed grating carries its glass on its own element: the grating branch takes the exit index from the element as written.
• ray_info_get returns the outgoing direction at the traced element.
• Centre of curvature is the vertex plus |Kr| along psiElt; KrElt is stored as −|R|.
Reference document: optical_design/SPECTROMETER_DESIGN_REFERENCE.md (forms, conditions, metrics, references).