## Slide 1
A VSWIR Dyson Imaging Spectrometer, Designed From the Spec
An EMIT-class push-broom spectrometer (F/1.8, 3000 × 500 pixels at 18 µm, 380–2500 nm) designed with MACOS from the public specification alone, scored on smile, keystone and the response functions, and checked by physical-optics propagation.
D. C. Redding, with Claude Code.
October 2026. Working record; no proprietary prescription is used.
DRAFT — in progress. Every number is from a committed, parameterized runner (mmacos, dyson5_run); records and figures are the runner's own output. Design of record: the compact variant (step R4): keystone 0.0026 px, smile 0.005 px, CRF 1.33 px, 76 % of the energy in one pixel, at a 220 mm block. The propagated point-spread function reproduces the ray centroids to 0.002 px, so these are the numbers a detector sees. The fold-prism layout (step R5) takes the detector package out of the slit's plane at CRF 1.27 px and 70 % in one pixel; a cold shield cannot be bought in this form, since every millimetre of air before the detector costs about 0.5 px of CRF. The block's size follows the slit: shared between two 27 mm modules, a 130 mm silica block of 1.6 kg with no meniscus images at the pixel (CRF 1.03 px) with half the record's air-glass crossings, against 220 mm, 8.2 kg and a 4 mm meniscus for one module.

## Slide 2
Contents
The target, the methods, the forms, the design ladder, the evidence
• 3 The target and how it is scored
• 4 The two methods, and the words used here
• 5 The Dyson as traced by the engine
• 6 The Offner as traced by the engine
• 7 The concentric Dyson and its scaling law
• 8 Two independent ray traces agree
• 9 The seed, scored
• 10 The departure ladder
• 11 The departure ladder, by the numbers
• 12 What each departure buys
• 13 The compact variant, as traced by the engine
• 14 The compact variant: the prescription
• 15 The compact variant in section
• 16 The compact variant, scored
• 17 The trade at a glance
• 18 The propagation twin
• 19 Slit diffraction loss
• 20 The fold prism, as traced by the engine
• 21 The fold prism: the prescription
• 22 The fold prism, scored
• 23 The cold shield: the air gap is the price
• 24 Where the design closes
• 25 How small can the block be
• 26 The block-size trade, by the numbers
• 27 The telescope that feeds the slit
• 28 Telescope and spectrometer end to end
• 29 Next steps
• 30 Run it yourself
• 31 Backup

## Slide 3
The target and how it is scored
Joe's specification, EMIT-class; the metrics stated once, here
item | value
F-number (air-equivalent, image space) | 1.8
focal plane | 3000 spatial × 500 spectral pixels, 18 µm
slit | 54 mm; spectral height 9 mm
band | 380–2500 nm, 4.24 nm per pixel
smile, keystone | < 0.1 pixel
SRF FWHM | < 1.5–2.0 pixels
CRF FWHM | < 1.5 pixels
radiometric chain | throughput, grating efficiency, QE, slit loss vs wavelength
• Smile: centroid drift along the slit at fixed wavelength; keystone: drift across wavelength at fixed slit position; both in pixels from ray centroids.
• SRF, CRF: slit ⊗ line-spread function ⊗ pixel ⊗ Airy, FWHM in pixels (Mouroulis & Green 2018 definitions); the Airy diameter at 2500 nm is 11 µm, under the 18 µm pixel, so the incoherent chain is valid.
• Design rules adopted from the literature: distortion to ~1 % of a pixel at design, > 75 % of the energy in one pixel, degraded spots accepted for uniformity, the grating is the stop.
• Realism (Jim): as-built SRF is 2.5–3 pixels, slits are 2 pixels wide, the systems are photon-limited; smile and keystone drive the design.
The 54 mm slit is 2.3× EMIT's; Table 3 of the review places this spec in the ALIS class (3200 spatial pixels, 380–2500 nm). Public comparison point: Carbon-I (arXiv:2505.22545), F/2.2, 2040–2380 nm.

## Slide 4
The two methods, and the words used here
Ray tracing scores the design; wave propagation checks it
• Ray tracing (MACOS, "the engine"): rays leave a point on the slit at one wavelength, refract through the block and meniscus, diffract at the grating into the design order, and land on the detector. The centroid of the landed rays per slit position and wavelength gives the field-angle and wavelength maps; their drift gives smile and keystone; the spread of the rays, convolved with the slit width and the pixel, gives the response functions.
• Wave propagation (the "twin"): the same prescription, but the light is carried as a complex wavefront. The ray trace sets the phase on a reference sphere before the detector; a Fourier transform propagates it to the detector plane and gives the point-spread function with diffraction. From it: the centroid again (checked against the rays), ensquared energy with diffraction, the response functions with diffraction.
• The chain: the geometric solver, in MATLAB, that lays out each form from its design conditions, solves the chief ray, the groove period and the focus by exact 3-D ray trace, and writes the prescription the engine traces. Engine and chain are checked against each other ray by ray.
• The ladder, steps R0–R5: the sequence of design freedoms added one at a time, each step re-solved and re-scored. Seed: the starting concentric design. Operand: a quantity the solver drives to a target. Trade: the one table that compares the steps.
• Ensquared energy: the fraction of a point image's energy inside one 18 µm pixel. SRF, CRF: spectral and cross-track response functions, the instrument's line shape in the two directions, quoted as FWHM in pixels.
Every number in the deck is a committed runner output; records are listed in Backup.

## Slide 5
The Dyson as traced by the engine
The concentric seed with every aperture declared: the beams clear every body; the grating is 270 mm wide on a 0.70 m radius and the slit sits 18 mm from the band
• The prescription: challenges/dyson5/dyson5_s1_dyson.in; bodies, rays and labels are read back from the engine. Radii are |R|; apertures are the declared circular radii (footprint plus 5 mm); z along the axis from the block's face.
E | name | type | surface | R (mm) | K | aperture r (mm) | z (mm)
1 | BlockFaceIn | Refractor | Flat | - | - | 32.1 | 0.5
2 | BlockSphereOut | Refractor | Conic | 220.0 | 0 | 73.2 | 220.0
3 | Grating | Grating | Conic | 708.4 | 0 | 142.6 | 708.4
4 | BlockSphereIn | Refractor | Conic | 220.0 | 0 | 73.2 | 220.0
5 | BlockFaceOut | Refractor | Flat | - | - | 32.4 | 0.5
6 | PreFPA | Reference | Flat | - | - | - | 1.3
7 | FPA | FocalPlane | Flat | - | - | - | 0.3
3-D view and the dispersion plane (Y-Z), metres, global frame.
• Clearance: the worst pair is the returning beam against the detector carrier, +1.11 mm with no cold shield; the slit sits at +6 mm and this wavelength lands at −12 mm on the same face.

## Slide 6
The Offner as traced by the engine
The all-reflective reference at F/2.8, re-posed at 0.22 R: the two mirror zones with the grating between the beams, clearing its mount by 10.2 mm
• The prescription: challenges/dyson5/dyson5_s1_offner.in, F/2.8, slit offset 0.22 R; the concave mirror used in two zones (E1, E3) with the convex grating (E2) at the stop; classical corrections: convex radius × 1.0034, second zone × 0.951 with a 0.3 mm offset.
E | name | type | surface | R (mm) | K | aperture r (mm) | z (mm)
1 | M1 | Reflector | Conic | 500.0 | 0 | 119.3 | -486.6
2 | Grating | Grating | Conic | 250.9 | 0 | 49.9 | -250.9
3 | M3 | Reflector | Conic | 475.5 | 0 | 113.2 | -463.8
4 | PreFPA | Reference | Flat | - | - | - | -0.8
5 | FPA | FocalPlane | Flat | - | - | - | 0.2
3-D view and the dispersion plane (Y-Z), metres, global frame.
• As corrected: keystone 0.028 px, CRF 1.20 px, SRF 3.69 px, 23 % of the energy in one pixel; the beams clear the grating's mount by 10.2 mm. It is the reference form and the ground where the propagation twin is validated (order 0: pupil OPD 8e-11 m, 85 % in one pixel).

## Slide 7
The concentric Dyson and its scaling law
The classical condition verified by exact trace; at this slit the concentric block needs r ≥ 213 mm
• The Dyson condition R_g = n·r / (n − 1) is the blur minimum by exact 3-D trace: 0.67 µm at the condition against 4–5 µm at ±5 %, image at −h, residual fifth order (h⁴·¹⁷, r⁻³·¹⁹).
• The scaling answer, before any element was added: a single concentric block meets a quarter-pixel corner blur only at r ≥ 213 mm, about twice flight scale, which is why the flight forms add an asphere, a meniscus or an air gap.
Rms blur at the slit corner (h = 28.2 mm) of a concentric silica Dyson at F/1.8 versus block radius, exact trace at order 0: blur ∝ r⁻³·¹⁹; the quarter-pixel budget is met at r = 213 mm (grating radius 687 mm).

## Slide 8
Two independent ray traces agree
The design solver and MACOS place every ray within a nanometre of each other, so the prescription is what the solver intended
• Two programs, one prescription. The design solver (MATLAB) lays out each form from its design rules and writes the prescription. MACOS then traces that prescription on its own. The check: every ray MACOS launches is re-traced by the solver through the same surfaces, and the two land within 1e-9 m at every surface; the dispersed band spans the detector to 1 %.
• The check is not trivial. With the aspheric block face of ladder step R2 the agreement is 1e-12 m per ray, while a solver that ignores the asphere misses by 0.26 mm.
• Wave propagation agrees too. On the Offner at order 0 the propagated point image is a clean Airy pattern, 85 % of its energy in one pixel, with a pupil error of 8e-11 m.
• What the checks found in MACOS, and fixed (details in Backup): glass names were ignored when a prescription loaded; propagation inside glass used the vacuum wavelength; a grating's groove spacing was held constant along the curved surface instead of along the chord; the grating's path-length term had the matching defect; the multi-wavelength optimizer's derivative loop overran its array on a spot-size target. Each now has a regression test written from the physics.
Regression tests: 15 in five classes plus the optimizer's; the MACOS fast suite stands at 510 pass, 0 fail (2026-10-01).

## Slide 9
The seed, scored
The concentric seed at a 220 mm block meets smile; keystone and the corner blur are the work
• Smile is met at the seed (below 0.01 pixel on both forms); the field-angle map is linear along the slit as designed.
• SRF sits at 2.02 pixels on both forms, the floor set by the 2-pixel slit; re-scored on the engine after the grating fixes (the earlier ramp with wavelength was the groove-period defect, not the design).
Scorer maps for the two seeds at 220 mm (rows: Dyson, Offner): field-angle map, smile (pixels), SRF FWHM (pixels), ensquared energy in one pixel, versus slit position and wavelength.

## Slide 10
The departure ladder
Each step solved on the exact chain with pixel-unit smile and keystone in the merit from the first pass, then emitted and scored in the engine
Engine-scored maxima per ladder step at the seed's 220 mm block (left: smile, keystone, CRF FWHM in pixels; right: minimum ensquared energy in one pixel against the 0.75 design rule).

## Slide 11
The departure ladder, by the numbers
Keystone falls 37-fold at fixed scale; the meniscus pays only with the block offset and grating radius moving with it
step | what moves | keystone (px) | smile (px) | CRF FWHM (px) | ensquared, 1 px | length (mm) | grating footprint (mm) | glass (L)
R0 | concentric seed | 0.095 | 0.006 | 2.28 | 0.44 | 708 | 275 | 22.2
R1 | grating-radius factor, face offset | 0.038 | 0.003 | 2.10 | 0.48 | 704 | 274 | 22.3
R2 | + conic and h⁴, h⁶ terms on the block face | 0.037 | 0.004 | 2.13 | 0.47 | 704 | 274 | 22.3
R3 | + block centre off the grating's, along the dispersion | 0.011 | 0.008 | 2.10 | 0.48 | 698 | 272 | 22.1
R4a | meniscus corrector alone | 0.063 | 0.012 | 2.49 | 0.33 | 698 | 270 | 22.3
R4 | meniscus with all variables (the compact variant) | 0.0026 | 0.005 | 1.33 | 0.76 | 694 | 269 | 22.7
R5 | + slit plate and fold prism: the detector out of the slit's plane | 0.0085 | 0.005 | 1.27 | 0.70 | 694 | 269 | 19.2
size alone | block radius free (341 mm) | 0.024 | 0.001 | 1.34 | 0.74 | 1099 | 427 | 82.8
SRF FWHM is 2.02–2.05 px on every step: the 2-pixel-slit floor. Length = slit plane to grating vertex; footprint = diameter of the grating hits over slit centre and ends × band edges; glass = the full hemispherical cap + meniscus, an upper bound: edged to its clear aperture the R4 block is a rod 147 mm across and 221 mm long, 3.7 L and 8.2 kg in silica. Record dyson5_s3_trade.txt.

## Slide 12
What each departure buys
De-concentring the block solves the distortion; the face asphere is inert; the blur is bought only by size or by the compact form
• Keystone: 0.095 → 0.011 pixels at fixed scale, nine times inside the 0.1-pixel specification and at the literature's 1 % design rule; smile stays below 0.01 pixel throughout.
• The block-face asphere does nothing here: step R2 converges to 10 nm sags, and a one-dimensional scan about R1 is a steep bowl centred at zero. An axisymmetric figure acts on every field point alike and cannot cancel a residual that grows as h⁴ along the slit.
• The blur does not move on any step, and the reason is on record: the dispersed image sits 12 mm from the order-0 image, so the slit corner's effective field height is about 32 mm, and the h⁴/r³ law predicts the measured 0.4 px rms.
• Two routes buy it: size alone (0.74 ensquared at a 341 mm block, 1.1 m long, 83 L of glass) or the compact variant: a meniscus corrector in the air gap, solved together with the block offset and the grating radius, reaches the same at the 220 mm block — 63 % of the length, 27 % of the glass.
The free-radius ladder: ensquared energy reaches the 0.75 rule only as the block grows to 341 mm.

## Slide 13
The compact variant, as traced by the engine
Step R4: the meniscus corrector in the air gap between the block and the grating; the design of record at a 220 mm block
• Eleven surfaces: the block's flat and spherical faces, the meniscus, the grating, and the same faces again on the way back to the focal plane; the element table is on the next slide.
• Clearance: the returning beam passes the detector carrier by 1.19 mm with no cold shield, and any shield fails the check; the fold prism of step R5 (slide 20) moves the detector out of the slit's plane.
3-D view and the dispersion plane (Y-Z), metres, global frame.

## Slide 14
The compact variant: the prescription
The eleven elements of step R4 as written in dyson5_s3_r4.in; radii are |R|, apertures the declared circular radii, z along the axis from the block's face
E | name | type | surface | R (mm) | K | aperture r (mm) | z (mm)
1 | BlockFaceIn | Refractor | Flat | - | - | 32.2 | 0.7
2 | BlockSphereOut | Refractor | Aspheric | 220.0 | -0.00650944 | 73.0 | 219.1
3 | MenA_out | Refractor | Conic | 1828.1 | 0 | 77.7 | 240.0
4 | MenB_out | Refractor | Conic | 2000.0 | 0 | 78.0 | 244.0
5 | Grating | Grating | Conic | 697.8 | 0 | 140.1 | 697.8
6 | MenB_in | Refractor | Conic | 2000.0 | 0 | 78.1 | 244.0
7 | MenA_in | Refractor | Conic | 1828.1 | 0 | 77.8 | 240.0
8 | BlockSphereIn | Refractor | Aspheric | 220.0 | -0.00650944 | 73.1 | 219.1
9 | BlockFaceOut | Refractor | Flat | - | - | 32.6 | 0.7
10 | PreFPA | Reference | Flat | - | - | - | 0.9
11 | FPA | FocalPlane | Flat | - | - | - | -0.1
The two block faces and the meniscus appear twice because the light passes them on the way out and back; the engine traces them as separate surfaces.

## Slide 15
The compact variant in section
Dispersion plane and slit direction, to scale: block, meniscus, grating; slit and focal plane on the block's face
Left: the dispersion plane, slit centre, rays at 380 / 1440 / 2500 nm (blue / green / red). Right: the slit direction, slit centre and ends at 1440 nm; the focal plane in magenta. Block shaded; 100 mm scale bar.
• Sizes: block radius 220 mm (217 mm thick, 85 mm face), meniscus 4 mm thick at radii near 2 m, grating 269 mm across on a 0.69 m radius; slit plane to grating vertex 694 mm.
• A global search over the meniscus (12 starts over its position, thickness and both curvatures, every R4 variable free) found four feasible basins at similar merit and none better on the detector: the lowest merit buys 0.0007 px of keystone, already 40× inside the specification, for +0.15 px of CRF and −0.10 of ensquared energy. The R4 of record stands.

## Slide 16
The compact variant, scored
Keystone 0.0026 px, smile 0.005 px, CRF 1.33 px, SRF 2.03 px; ensquared energy 0.76 geometric and 0.75 with diffraction
• Checked by propagation: the point-spread function's centroid equals the ray centroid to 0.0022 px along the dispersion and 0.0003 px along the slit at every slit position and wavelength, so a detector sees these numbers.
Engine-scored maps for R4 on 18 µm pixels, per slit position and wavelength: field-angle map, keystone, smile, SRF FWHM, CRF FWHM, ensquared energy; each convention on its colorbar, maxima in the labels.

## Slide 17
The trade at a glance
Distortion, response functions and ensquared energy per step, both records and the fold; the specification and the literature rules as lines
Left: keystone and smile maxima (log scale) against the 1 % rule. Middle: CRF and SRF FWHM against the 1.5 px specification and the 2-px-slit floor. Right: minimum ensquared energy in one pixel against the 0.75 rule. Steps R0–R4 at the held 220 mm block, R0–R2 with the block radius free, and R5 with the fold prism.

## Slide 18
The propagation twin
A far-field terminal on a reference sphere, re-posed per slit position and wavelength, agrees with the ray centroids to 0.0013 px
• What it checks: the ray-side scorer's centroids and response functions against physical-optics propagation through the same decks; across a grating the comparison is made in phase (modulo λ), never as unwrapped lengths.
Left: the Offner at order 0, PSF (log scale) with the 18 µm pixel box, 85 % ensquared. Middle: wave-minus-ray centroid over the slit and band, Offner and Dyson seeds. Right: SRF and CRF from the propagated PSF at the slit centre.

## Slide 19
Slit diffraction loss
A 36 µm slit at F/1.8: 0.3 % of the light misses the grating at 380 nm and 1.8 % at 2500 nm, by the engine and by the closed form alike
• The model: a uniformly lit 36 µm slit of zero length, propagated as a far-field wave to the grating's plane 0.70 m away; loss = the energy landing outside the F/1.8 acceptance. The closed form is the exact sinc² integral for the same slit and acceptance.
• The engine reads 1.04 / 1.14 / 0.90 / 0.86 × the closed form at 380 / 700 / 1440 / 2500 nm once two conditions are met, each found by a one-knob test: the far-field window at least twice the acceptance (a window 11 % wider than the acceptance folds the diffracted tail back inside and reads 0.3× at 380 nm), and the energy normalised to the propagating region |sin θ| ≤ 1 (the planar transform carries 0.7–1.3 % of the energy beyond it at the long end and read 1.36× at 2500 nm). The residual at the long end is the grid pitch across an acceptance only four sidelobes wide.
• The number for the radiometric chain: loss past the grating 0.28 % at 380 nm, 0.5 % at 700, 1.0 % at 1440, 1.8 % at 2500 nm (closed form; the engine reads 0.29 / 0.59 / 0.94 / 1.57 %). The telescope's cone is not yet in the model; the literature puts the partially coherent case near 10 %.
Loss past the grating versus wavelength: engine far-field leg (points) against the sinc² form (line).

## Slide 20
The fold prism, as traced by the engine
Step R5: a slit plate and a mirror-coated fold prism cemented to the block; the detector 27 mm from the slit, every clearance pair positive
• The form: the slit stands 1 mm in air before a 24 mm plate cemented to the block's face; under the image a prism with a 45° mirror-coated plane 16 mm below the face folds the beam away from the slit, and the detector sits 1 mm in air beyond the prism's exit face (E11–E14 in the table on the next slide). Total internal reflection is not available: at F/1.8 in silica the marginal rays reach 30° against a 43.6° critical angle, so the fold is a coated mirror inside the glass.
• Solved as a ladder step: R4's eleven variables plus the slit plane's axial position, the face offset bounded at the fold's scale, warm-started from R4; the groove period and the focus re-solved at every iterate.
• Clearance: the detector package (54 × 9 mm plus a 5 mm carrier, 10 mm deep) is 27 mm from the slit; the worst pair is the package against the fold mirror's mount at +0.90 mm. Record dyson5_s5_r5_h00.in.
3-D view and the dispersion plane (Y-Z), metres, global frame; E11 is the fold mirror, E13 the pre-detector reference, both below the block's face.

## Slide 21
The fold prism: the prescription
The fourteen elements of step R5 as written in dyson5_s5_r5_h00.in; radii are |R|, apertures the declared circular radii, z along the axis from the slit
E | name | type | surface | R (mm) | K | aperture r (mm) | z (mm)
1 | PlateIn | Refractor | Flat | - | - | 32.3 | 1.0
2 | BlockFaceIn | Refractor | Flat | - | - | 37.0 | 25.0
3 | BlockSphereOut | Refractor | Aspheric | 220.0 | -0.00657465 | 73.3 | 221.9
4 | MenA_out | Refractor | Conic | 1971.2 | 0 | 77.6 | 240.0
5 | MenB_out | Refractor | Conic | 1980.0 | 0 | 78.0 | 244.0
6 | Grating | Grating | Conic | 694.0 | 0 | 139.3 | 694.0
7 | MenB_in | Refractor | Conic | 1980.0 | 0 | 78.0 | 244.0
8 | MenA_in | Refractor | Conic | 1971.2 | 0 | 77.7 | 240.0
9 | BlockSphereIn | Refractor | Aspheric | 220.0 | -0.00657465 | 73.4 | 221.9
10 | BlockFaceOut | Refractor | Flat | - | - | 37.3 | 25.0
11 | FoldMirror | Reflector | Flat | - | - | 35.3 | 9.0
12 | PrismExit | Refractor | Flat | - | - | 32.7 | 9.0
13 | PreFPA | Reference | Flat | - | - | - | 9.0
14 | FPA | FocalPlane | Flat | - | - | - | 9.0
The plate (E1–E2) and the block face (E2, E10) are glass to glass: the engine traces the cemented face as a refraction between equal indices. The fold mirror (E11) is a reflector inside the glass; after it the axis runs along −y, so E12–E14 share the fold's z and stand at y = −20 to −21 mm (slit at y = +6 mm). Groove period 114.4 µm.

## Slide 22
The fold prism, scored
Keystone 0.0085 px, smile 0.005 px, CRF 1.27 px, SRF 2.04 px; 70 % of the energy in one pixel
• Against the compact variant: CRF 1.33 → 1.27 px and keystone 0.0026 → 0.0085 px, both well inside the specification; ensquared energy 0.76 → 0.70, under the literature's 0.75 rule. A refinement from the same basin at twice the iterations reached 0.73 with CRF 1.32 px, so the trade between the two is real and small.
Engine-scored maps for R5 on 18 µm pixels, per slit position and wavelength: field-angle map, keystone, smile, SRF FWHM, CRF FWHM, ensquared energy; each convention on its colorbar, maxima in the labels.

## Slide 23
The cold shield: the air gap is the price
A shield of height h needs h + 1 mm of air before the detector, and every millimetre of air costs about 0.5 px of CRF
• Measured on the compact variant before any re-solve: widening its 0.85 mm air gaps at slit and detector to 2 and 3 mm takes the CRF from 1.33 to 1.78 and 1.96 px and the keystone from 0.02 to 0.23 and 0.42 px. Physics, not the solver: a plane air-to-glass boundary ahead of an F/1.8 cone carries spherical and field aberration that grows with the gap, which is why Dyson slits and detectors are proximate.
• The sweep: shield heights 0, 1, 2, 3 and 5 mm, the same gap on the slit side to keep the object and image media equal, a full twelve-variable re-solve at each, scored in the engine and run through the clearance gate with the package in the folded frame. Every point clears; the CRF climbs 1.27 → 1.75 → 2.31 → 2.78 → 3.75 px and the re-solve does not recover it. The record is the tallest shield that closes: none.
• What that leaves: a shield inside the 1 mm the design tolerates; a cold window cemented as the prism's exit face with the shield as the detector housing behind it (the next R5 variant); or a slower cone, since the F/2.2 point of the closure envelope has CRF 1.15 px at R4 and could spend some of it on air.
Per cold-shield height: CRF and SRF FWHM against the 1.5 px specification (left), minimum ensquared energy against the 0.75 rule (middle), the clearance margin and the plate thickness the solve chose (right); the star is the refined 0 mm point.

## Slide 24
Where the design closes
The compact variant re-solved one parameter at a time from the record: F/1.8–2.2, blocks of 220–300 mm, slits to 54 mm, both pixels and both glasses close
• Method: from the R4 of record, one axis at a time, every point a full eleven-variable re-solve on the exact chain, then emitted and scored in the engine. A point closes when smile and keystone are under 0.1 px, CRF under 1.5 px, SRF under 2.0 px and no variable sits on a bound. The detector stays 54 × 9 mm; the pixel count follows the slit length and the pitch.
• Outside the envelope the first metric to fail is the CRF: 2.37 and 1.61 px at 150 and 180 mm blocks (the h⁴/r³ law of the scaling slide), 1.55 px at a 60 mm slit (by 0.05 px). F/1.6 and F/2.8 end on the meniscus bounds with the CRF itself at 1.37 and 1.07 px: a bound to widen, not a form that fails. Smile and keystone never exceed 0.02 px on any point. A 30 µm pixel or a CaF2 block puts all of the energy in one pixel; the corner, F/1.6 with a 150 mm block, does not close.
Each metric divided by its limit (1 = the limit) along five axes; a red cross marks a point that does not close (over a limit or on a bound).

## Slide 25
How small can the block be
The slit is the lever: shared between two 27 mm modules the block falls from 220 mm to 130 mm or less, and the meniscus is no longer needed
• Why the record is 220 mm thick: in the Dyson form the flat face sits at the center of curvature, so the block's thickness is its radius, and the blur law of the scaling slide (h⁴/r³) ties the radius to the slit length.
• The trade: each point is a full re-solve walked down in radius, warm-started from the next larger block and scored in the engine, with the meniscus (solid lines, step R4) and without it (dashed, step R3); a filled marker meets the specification and a ringed one also matches the record's own scores.
Per block radius: CRF (left), ensquared energy in one pixel (middle), mass of the edged block (right); solid lines with the meniscus, dashed without; filled = meets the specification, black ring = matches R4 of record.

## Slide 26
The block-size trade, by the numbers
Two modules with no meniscus: a 130 mm silica block at 1.6 kg images at the pixel with half the air-glass crossings of the record
configuration | block radius and thickness (mm) | edged mass (kg) | air-glass crossings, uncoated throughput | CRF (px) | ensquared, 1 px | smile / keystone (px)
R4 of record: silica, one 54 mm slit, meniscus | 220 | 8.2 | 8, 0.76 | 1.33 | 0.76 | 0.005 / 0.003
CaF2, one 54 mm slit, no meniscus | 240 | 14.3 | 4, 0.88 | 1.21 | 0.82 | 0.005 / 0.006
silica, two 27 mm slits, no meniscus | 130 | 1.6 each | 4, 0.87 | 1.03 | 1.00 | 0.007 / 0.009
silica, two 27 mm slits, no meniscus, smallest matching the record | 100 | 0.9 each | 4, 0.87 | 1.25 | 0.80 | 0.008 / 0.012
CaF2, two 27 mm slits, no meniscus, smallest matching the record | 80 | 0.9 each | 4, 0.88 | 1.02 | 1.00 | 0.002 / 0.007
• The meniscus was paying for the long slit. With one 54 mm slit, silica closes only with the meniscus, a plate 4 mm thick and 155 mm across that the solve wants thinner still; the thicker meniscus designs of the global search (about 30 mm) miss the specification at CRF 1.64 and 1.72 px. Without a meniscus, one module closes only in CaF2 and only at 240 mm and 14 kg.
• With two modules it is not needed: the plain block matches the record from 220 mm down to 100 mm in silica and 80 mm in CaF2, with four air-glass crossings where the record has eight, 15 % more light before any coating, and no thin part to make, mount or shake. CaF2 still images at the pixel at 80 mm, where silica has fallen to CRF 1.49 px; silica needs 130 mm for the same image. An 80 mm CaF2 block or a 130 mm silica block is a materials choice the ray trace cannot make.
• What two modules cost: two gratings and two detectors of 1500 pixels, and a swath split ahead of the slits, since each block is wider than its slit and the slits cannot abut. The slit-to-detector clearance stays near 0.5 mm at every size. Halving the glass path also halves the wavefront error from index inhomogeneity and thermal gradients, estimated at 0.4 waves each for the 220 mm block.
Record dyson5_size.txt (CCMac, 2026-10-02): 48 engine-scored points; throughput is the uncoated Fresnel product at 1 µm, normal incidence; the Mac's engine reproduces the Linux record of R4 to four decimals.

## Slide 27
The telescope that feeds the slit, at Jim's numbers
f = 330 mm, 183 mm at F/1.8, 9.4° per 3k module or 4.7° per 1.5k; three forms traced in the engine, none yet packaged at the pixel
• The target moved. Jim's 30 m ground sample from 550 km on 18 µm pixels sets f = 330 mm and 183 mm at F/1.8; the swath is 9.4° cross-track for a 3k module, 4.7° for a 1.5k one, with a telecentric, flat image on the slit. The EMIT-parameter three-mirror of the earlier beat (f = 126 mm, 24.6°, 67 px at the slit) stands as the layout and end-to-end machinery; the designs below are at the new numbers.
• The coaxial three-mirror parent (two routes). The chain's offset solves at 9–10° leave a field-constant residual — the parent's own aberration off its axis — 2 944 nm at best with the clearance gate failing, 6–65 px rms spots in the engine. The design layer's Korsch TMA with conics solved by the native optimizer at a scanned bias is diffraction-limited on axis (0.008 waves) and holds to ±1.5°: at 1° bias the strip centre is 0.41 px but the imageable half-field is a third of the swath, and the bias cannot be raised to unobscure. Three conics do not correct 9.4° at F/1.8 on the coaxial form. The unobscured eccentric section of the same parent (pupil decentered 205 mm, the beam passing below M2 to M3 and a focal plane beside it, no hole, no central obstruction) is the first packaged imaging telescope in the record: three conics hold the 1.5k strip at 8.9 px (4.3 px at the strip centre), every body clear, 1.05 kg of mirror — at a plate scale of 447 mm, not the 330 mm the ground sample asks. Asked to hold the plate scale too (the optimizer's new per-field image-position rows), the same three conics give up the blur: blur and plate scale compete, and the 3k strip's ends sit at 10 mm on this form. Both modules need more than conics: aspheres through the native optimizer, or freeform.
• The two-mirror modified Schwarzschild (the review's form for this regime). Convex primary, concave secondary, the stop virtual at M2's front focus so the output is telecentric; closed-form first order, exact chain, engine equal to chain on every ray. On axis — obscured, M1 in the image cone — it images: 1.10 px max rms spot for the 1.5k module (0.59 on axis), 4.26 px for the 3k, each solved on its own strip with M1 and M2 aspheres, the review's own TMS scaled to this focal length sitting at 2.3–4.6 px. It packages only with the strip 30° off axis: with the clearance operand made smooth (an exact segment-to-disc distance and a softmin over rays, where a sampled minimum had stalled every step) the packaged solves reach 123 px (1.5k, +5.4 mm clear) and 178 px (3k, +4.8 mm) and stall at the wall's knee. The bound settles it: with the wall switched off, the same 30° layouts still sit at 25 px (3k; and the 1.5k solve ran pathological) — the form, not the solver, is out at this bias. Verdict: no packaged Schwarzschild images at the pixel at f = 330 mm, F/1.8; no end-to-end row for it.
Left: the packaged unobscured section of the TMA parent for the 1.5k module (step 2b, 205 mm decenter, 3° bias, clearance +0.1 mm), YZ and XZ as the design layer renders it — M1 above, M2 below the incoming beam, the intermediate focus, M3, the focal plane beside it. Right: the same section at 170 mm for the 3k strip, whose ends do not image.

## Slide 28
Telescope and spectrometer end to end
One prescription of 16 (R4) and 19 (R5) elements, the grating its stop; the spectrometer's scorer sees the telescope's blur
• The deck. The telescope's surfaces are prepended to the spectrometer of record — sky, M1, M2, M3, fold, the slit as a pass-through reference, then block, meniscus, grating and detector — with a collimated 70 mm source per field and the grating declared the stop. Gate tTelescopeRx: every ray at the slit and at the detector within 1e-9 m of the design solver's.
• The score (7 fields × 7 wavelengths, the spectrometer's own scorer): with R4 smile 3.1 px, keystone 0.59 px, SRF 15.7 px, CRF 15.5 px; R5 the same to 0.03 px. Against the spectrometer alone (smile 0.005, keystone 0.003, CRF 1.33 px) these are the telescope's 67 px blur passing through. Clearance across both +0.75 mm with R4; with R5 the fold mirror's blur-widened footprint meets the detector package at −0.11 mm.
• What it establishes: the end-to-end machinery is in place and gated — a telescope deck of record, a combined prescription with the stop at the grating, the admitted fraction per field, the clearance gate across both instruments. Records dyson5_t2.txt, decks dyson5_t2_r4.in, dyson5_t2_r5.in.
3-D view and the dispersion plane (Y-Z), metres: the folded telescope below the slit plane, the block, meniscus and grating (E10) above it along the Dyson's axis, the detector on the block's face.

## Slide 29
The 1.5k telescope through its Dyson
On the telecentric parent every field is admitted and the plate scale holds; the strip's inner half images at 2–10 px, its edges at 19 px
• The pupil is a first-order condition. The section's exit pupil must sit near infinity to feed the near-telecentric Dyson (its chiefs cross 14–44 m away; it accepts chiefs within 0.09° of its own). A Korsch with a real intermediate focus between M2 and M3 can never be telecentric, so the layout was re-posed with M3 in front of that focus (the Cook/EMIT form, tma_layout 'telecentric'): on that parent's section the chiefs are within 0.5° across the strip, the pupil ~1 m out, every field admitted (0.997–1.000), the plate scale calibrated to the spec by the parent's f-number.
• The figure stage (h⁴+h⁶ on all three mirrors, the per-field image positions as targets, scored on the corrected engine): at 4° bias and 190 mm decenter — the point the clearance walk selects — the strip images at 2.1 px at the centre, 4.2 / 9.8 px at ±0.8° / ±1.6°, 19 px at the ±2.3° edges (best-focus rms 37 / 75 / 176 / 343 µm), plate scale 333.8 mm, clearance +3.97 mm with the mount counted once.
• Through the 130 mm module (the Dyson rolled 180° about the chief to clear its detector package from M2): 98.8 % of the swath on the slit, every field admitted, smile 3.26 px, keystone 0.63 px, CRF 15.5 px, SRF 5.9 px — the telescope's edge blur seen through the Dyson, the same at every wavelength. Chain and engine agree to 1e-14 m.
• The 3k section (4° bias, 180 mm) closes its scale and distortion — 326.8 / 319.2 mm, 100 % on the 54 mm slit, smile 10.6 px, keystone 1.37 px — with its edge fields at 1.23 mm (68 px). Records dyson5_tA_B3_.txt, dyson5_t5e_tA_B3_.txt.
The 1.5k telescope through its Dyson (dyson5_t5e_tA_B3_1k5_b4d190_B1), per slit position and wavelength: the field-angle, keystone and smile maps, the spectral and spatial response widths, and the energy in one pixel. The response widths rise at the two strip ends and nowhere else.
Supersedes the 2026-10-04 row (1.3 / 15.8 px): that solve's aperture circle clipped the edge fields (Backup, finding 10).

## Slide 30
What limits the strip edge
Cross-track astigmatism of the eccentric section, growing as the square of the field; untouched by focus, by the mirrors' power split, or by astigmatism terms alone
• It is not the metric. The optimizer's default merit, the path length to each ray's own point on the detector (which the chiefs meet at 31°), floors at 16 µm at every field and ranks the strip edge at 2.1× the centre where the true reference sphere ranks it 13.7×. Re-solving the same conics and aspheres on the true sphere moves the edge 343 → 332 µm, 3 % — inside the solver's run-to-run scatter. The reference sphere is the reporting metric from here on (about the detector point, and about best focus; they answer different questions).
• It is not focus, and not the field curvature of the parent. Along the strip the along-track focus is flat at every secondary magnification; the cross-track focus curves 2–4 mm, and the two line foci at the edge sit 2.2–5.3 mm apart. The parent's Petzval sum predicts a flat field near m₂ = 2.9 and the engine shows none there; the magnification that flattens the mean focus (m₂ = 6) is 2× worse once solved. m₂ = 3.0 is modestly better than the 3.5 used so far (edge 343 → 291 µm) and is the parent for the freeform work.
• It is not astigmatism terms alone. With the aspheres carried exactly on each mirror and Zernike astigmatism added about each section's pole, the edge does not move (291 → 297 µm): those terms are field-constant, the defect is field-quadratic (line-focus separation 0 / 0.9 / 2.1 mm at 0° / 1.6° / 2.3°). The field dependence enters through the footprint's walk across each mirror times its higher terms — coma and trefoil, then the symmetric terms — the steps now running.
step | edge rms spot | edge wavefront (sphere about detector point / best focus) | line-focus separation at the edge
conics + aspheres, m₂ = 3.5 | 343 µm | 33.9 / 26.8 µm | 2.8 mm
same, solved on the true sphere | 332 µm | — / 25.7 µm | —
conics + aspheres, m₂ = 3.0 | 291 µm | 27.9 / 23.0 µm | 2.2 mm
+ Zernike astigmatism, m₂ = 3.0 | 297 µm | 27.8 / 23.5 µm | 2.3 mm
1.5k section at 4° bias, 190 mm decenter, ±2.34° field; wavefront rms over the pupil at 633 nm; the two line foci from the x- and y-slices of the bundle along the chief. Records dyson5_tA_EP_cp*.txt, dyson5_tA_pz_1k5.txt, dyson5_tA_FF_1k5.txt.

## Slide 31
Next steps
The native optimizer on the record, the cold window, and the telescope that feeds the slit
• The native multi-wavelength optimizer (MACOS CALIB) confirms the compact variant: the engine's spot-size solve over 5 slit positions × 6 wavelengths, the double-pass copies of each surface linked as one, smile and keystone held as walls between iteration chunks, the engine's design read back under an identity check (2e-16 m). With the blur freedoms (block face radius and conic, meniscus faces, focus) every step is rejected: R4 is a local optimum of the engine's merit as well as the chain's. With the grating's position free the engine bought blur with 15 px of keystone in five iterations and the wall rejected it: the reason the design needs distortion operands, queued as an engine feature. From a deliberate 0.3 mm defocus the same solve cuts the spot from 97 to 21 µm, so it moves when there is something to gain. The block's asphere joins the freedoms now that its differential step is fixed (Backup).
• The cold window: the R5 variant with the shield as the detector housing behind a window cemented as the prism's exit face, under the same clearance gate.
• One module or two (a project decision): one 54 mm module needs the 220 mm, 8 kg block and its thin meniscus; two 27 mm modules need a plain 130 mm block of 1.6 kg each, with the swath split ahead of the slits. The choice also sets the telescope's field: 24.6° for one, or 12.3° each for two.
• The radiometric chain against the band: throughput, grating efficiency, detector quantum efficiency and the slit loss above.
• The telescope's image: the unobscured section of the telecentric three-mirror parent packages and holds the 1.5k strip's inner half at 2–10 px with its plate scale and every clearance; the strip edges (19 px at ±2.3°, 68 px at ±4.7° for 3k) are cross-track astigmatism that no symmetric surface term reaches. Running now: the freeform steps on the m₂ = 3.0 parent — coma and trefoil, then the symmetric terms, warm-started step to step on the true reference sphere; then the same for the 3k module; then the end-to-end row with each module's Dyson. Queued in the engine: the fixed-station reference sphere for the optimizer on near-telecentric designs, and the asphere + Zernike surface as one emitted option.
• Future work, once the design of record is stable: a surface-by-surface tour of the prescription (role, ray footprint, clearance, and the field where a propagation leg ends, per surface); spot diagrams in the Mouroulis & Green form, slit positions down and wavelengths across inside the 18 µm pixel box; the telescope and the end-to-end instrument; polarization sensitivity of the Dyson against the Offner, since the Dyson's near-normal incidence is what the literature credits for its low sensitivity; and, once the telescope exists, full diffraction from the slit through the grating to the detector, to put a number on the slit's truncation of the telescope's image (the literature expects about a 10 % effect on the response functions).

## Slide 32
Run it yourself
One parameter file, one runner, every stage through it
cd <path>/MACOS_resources/mmacos % the mmacos folder of the repository (the engine is built already)
matlab % start MATLAB here
>> run('mmacos_setup.m'); % puts the engine and the design tools on the path
>> addpath('challenges/dyson5');
>> OUT = dyson5_run(); % stage s0 only: the scaling law, no engine needed
>> OUT = dyson5_run(struct('stages', {{'s1','s2','s3'}})); % emit the decks, score them, run the ladder
>> OUT = dyson5_run(struct('stages', {{'s5','s4env'}})); % the fold prism sweep; the closure envelope
>> OUT = dyson5_run(struct('Fno', 2.0, 'block_r_m', 0.25, 'stages', {{'s1','s2','s3'}})); % your own instance
• Changeable design parameters live in one file, dyson5_params.m: F-number, pixel count and pitch, band, slit width in pixels, block radius, glass, diffraction order, the slit offset, the ladder's steps and weights, the aperture and mount margins, the detector package, the fold's depth and the cold-shield height. Pass any of them as fields of the struct to drive a different solution; every record in this deck is a stage output under challenges/dyson5/.
• Where designs close (slide 24): F/1.8–2.2, block radii 220–300 mm, slits to 54 mm, 18 and 30 µm pixels, silica and CaF2, each a full re-solve scored in the engine; outside, the CRF fails first (150 and 180 mm blocks, the 60 mm slit), and F/1.6 and F/2.8 end on the meniscus bounds. Also on the record: block radii 50–500 mm at order 0 for the scaling law, and the Offner reference at F/2.8.
• Checks: ./run_mmacos_tests.sh tSpectrometerRx and the four grating, glass and propagation classes, all in the fast suite.

## Slide 33
Backup
Diagnostics, the engine findings, and the conventions behind the main path.

## Slide 34
Backup: eight engine findings, each with a regression test
Found by the challenge's checks on 2026-09-30 to 10-03, fixed in the engine the same day
finding | symptom | fix | test
glass names ignored at load | a GlassElt= Silica element traced as air in every binding | the glass catalog is blanked once at allocation, not on every load | tGlassDispersion (3)
vacuum wavelength inside glass | a propagation leg in a medium ran at the wrong Fresnel number by n | every kernel takes λ/n of the leg's medium | tPropMedium (3): z in n ≡ z/n in vacuum
groove period along the surface | 2.8 / 3.3 px rms spectral blur at 2500 nm (Offner / Dyson) | the local grating vector is the un-normalised projection of the ruling direction (chord-ruled) | tGratingImmersed (4), test_grating_chord
grating path-length jump | 4 waves rms of pupil OPD where the rays converged to 0.05 µm | the jump is the groove count from the vertex along the ruling direction | tGratingOpl (2)
optimizer derivative stride | a spot-size optimisation over several fields overwrote memory on its second field (the derivative columns advanced by the wavefront's size, not the objective's) and crashed or hung the host | advance by the objective's size, as the value loop does | tSpectrometerRx native leg, tDesignTelescope (70, unchanged)
ray behind the surface after a pupil reference | a two-mirror whose entrance-pupil reference sits 5 mm ahead of its convex primary scattered every ray but the chief in a one-call trace (93 mm rms), while an element-by-element trace was right — by accident | the root of the conic after a reference is the one whose hit point is nearest the element's reference point (its vertex, or an off-axis section's pole), not the one whose length matches the ray's distance to the vertex (which the ray's height dominated); a restarted trace resets its "previous element" per ray | tTraceRestart (2) on the deck itself; exit-pupil radii unchanged to the bit on four decks
beam conditions only under a beam target | the chief's direction and position at an element could not be scored with a spot or wavefront target, one target served every field, and a multi-field beam solve scored the last field alone | the beam rows ride on any target; a position target per field; a weight; the ray centroid as the position | tBeamRows (3): telecentric under a spot target, two fields met by one piston, centroid vs chief
optimizer asphere step and failure exit | an aspheric coefficient was probed by a fixed 1e-10, round-off on a deck in metres: a zero derivative column, a singular matrix at the first step, and a stop on that path that ended the MATLAB process | the step is 1e-3 of the coefficient (sag-based for a zero one); the failure restores the optics and returns a flag | tAsphCalib (2): a spoiled paraboloid driven back to zero; the failure path with the host alive
Flat gratings are unchanged by the grating fixes; the wavefront-target optimizer, which every telescope design used, was never affected by the fifth. A seventh item, a short AsphCoef= line killing the host process, now pads with zero and warns (tRxShortAsph); the same guard for ZernCoef= is queued.

## Slide 35
Backup: four more findings from the telescope's eccentric section
Found 2026-10-04 to 10-05, each invisible on a coaxial design, each fixed the same day
finding | symptom | fix | test
ray on the far sheet of a hyperboloid | 40 of 1185 rays on the section's M3 (sheets 22 mm apart) took the second sheet: 44 mm of extra path, a 10 mm spot tail, every ray reported as passing — 7.8 mm rms wavefront at the focal plane while an outlier-cut spot read 400 µm | the intersection is the root on the sheet the vertex is on (the normal's axial component keeps the sign it has at the vertex); first crossing on a tie; the first crossing alone is wrong, since M2's far sheet sits in the beam | tFwdRoot (5); 406 decks pre/post identical
optimizer aperture sized at one field | the circle declared for the asphere solve enclosed the nominal field's footprint only; the strip-edge fields lost every ray on M3 and were dropped by the solve (the 9.9999e36 sentinel), which then drove M3's conic blind to them | the circle encloses the footprint over every field of the solve | tAsphHook (3): its first pin was the wavefront of the surviving rays; re-pinned
stop aimed at the parent vertex | the exit-pupil finder and the optimizer set the stop on M1 with no offset; on an eccentric section that is the parent vertex, 190 mm from the beam, and the pupil sphere was placed for the wrong beam | the stop at the deck's object-space stop point | tStopApStop (4)
Zernike origin at the parent vertex | the emitter placed each mirror's Zernike origin at its vertex while the axes were the section pole's, so freeform terms on a section were evaluated 3.8 radii outside the unit disc (1 µm of defocus moved the chief 0.19 mm instead of 0.005) | the origin is the element's pole | tFreeformPole (3)
Every one of the four passed every existing check: the rays "passed", the solve "converged", the deck loaded. What exposed them was a section whose beam is 190 mm from its parent's vertex — the first design in the record where the vertex and the lit patch are not the same place.

## Slide 36
Backup: records and tools behind each slide
Every number traces to a runner stage and its record file
slide | runner stage | record | tool
scaling law | s0 (engine-free) | dyson5_s0_scaling.txt | design/src/dyson_layout.m, dyson_scaling.m
as traced (every form) | dyson5_view_figs.m | _view3d.png, _viewyz.png | macos.view_rx on the deck
seed scored | s1 emit, s2 score | dyson5_s1.txt, dyson5_s2.txt, dyson5_s2_maps.png | spectrometer_geom.m, spectrometer_rx.m, spectrometer_score.m
chain vs engine | gate | tests/tSpectrometerRx.m | per-ray re-trace, 1e-9 m
propagation twin | s2w (opt-in, model 512) | dyson5_s2w.txt | spectrometer_wave.m
departure ladder, R4, trade | s3, s3free, s3b | dyson5_s3.txt, dyson5_s3free.txt, dyson5_s3_trade.txt, dyson5_s3_layout_r.png, dyson5_s3_maps_r.png | dyson_ladder.m, dyson5_trade.m
meniscus search | tool | dyson5_s3_r4global.txt | dyson_r4_global.m
slit loss | s2l + tool | dyson5_s2l.txt, dyson5_s2l_tests.txt, dyson5_s2l_slitloss.png | far-field leg vs sinc²; dyson5_slitloss_tests.m
fold prism, cold shield | s5 | dyson5_s5.txt, dyson5_s5_r5_h*.in, dyson5_s5_maps_r5.png, dyson5_s5_sweep.png | spectrometer_geom.m (form dyson_fold), spectrometer_clearance.m
closure envelope | s4env | dyson5_s4env.txt, dyson5_s4env.png, dyson5_s4env_*.in | dyson5_envelope.m
native optimizer | s4 | dyson5_s4.txt, dyson5_s4_r4n_seed.in (the CALIB deck), dyson5_s4_r4n.in | dyson_native.m
block-size trade | dyson5_size_trade.m | dyson5_size.txt, dyson5_size.png, dyson5_size_*.in, BRIEF_dyson5_size.md | continuation walks over dyson_ladder.m
telescope, three-mirror at Jim's numbers | t3s, t3w, t3o, t3e | dyson5_t3*.txt, BRIEF_dyson5_beat5c.md | tma_screen, the offset solves on telescope_geom.m
telescope, modified Schwarzschild | t4 | dyson5_t4.txt, dyson5_t4_r2c_.in, _view.png | tms_paraxial.m, tms_firstorder.m, tms_geom.m, tms_clear.m
telescope, TMA parent by the design layer | dyson5_tma_step1.m | dyson5_tma_step1.txt, dyson5_tma_step1_layout.png, BRIEF_dyson5_tma.md | macos.design.tma_layout, Telescope, CALIB
end to end at Jim's f-number (informative) | t5e | dyson5_t5e_1k5.txt, dyson5_t5e_1k5_e2e.in, dyson5_t5e_1k5_maps.png | tel_deck_geom.m (the exact chain from a Telescope deck), the spectrometer's scorer
telescope, telecentric parent: first order, figure, decenter walk | tA (stages A, B, re-run) | dyson5_tA_B3_.txt, dyson5_t5e_tA_B3_.txt/.png, decks per point | tma_layout 'telecentric', Telescope.optimize with aspheres and position rows, spectrometer_clearance (mount once)
strip edge: metric, Petzval, freeform steps | tEP, tPZ, tFF | dyson5_tA_EP_cp1/cp2*.txt, dyson5_tA_pz_1k5.txt, dyson5_tA_FF_1k5.txt, BRIEF_to_dyson5.md addenda 42–44 | the reference-sphere evaluator and solver (tEP_strict_solve_), the line-focus probe, FreeForm decks with the asphere in the Mon channel and the Zernikes about the pole
telescope, TMA unobscured section (step 2/2b, Linux) | dyson5_tma_step2_linux.m | dyson5_tma_step2_linux_d170.txt, _d190.txt, dyson5_tma_step2b_linux_d205.txt, _d205_1k5.in, _layout_*.png | Telescope.set_offaxis, CALIB over the strip with the per-field position rows, check_clipping
Conventions behind the scaling law: block index n(silica, 1 µm) = 1.450417; in-glass marginal half-angle u = asin(1 / 2nF); field height h from the Dyson axis on the flat face; the slit corner is h = hypot(27 mm, 8 mm).

## Slide 37
Backup: conventions pinned on the way
Engine facts the chain depends on, stated once
• ChfRayPos is where rays start and must lie before the first surface; at load the engine folds zSource in once, after which it is the physical source.
• macos.stop aims immediately and its first pass is one step short on this deck (3.6 mrad): declare the stop first, then write the exact chief ray.
• A Return coincident with the focal plane drops the rays; use a Reference upstream.
• A reflector inside glass (Element= Reflector carrying GlassElt=) is honoured: the fold mirror of step R5 lands every ray to 1e-9 m against the chain.
• An immersed grating carries its glass on its own element: the grating branch takes the exit index from the element as written.
• ray_info_get returns the outgoing direction at the traced element.
• Centre of curvature is the vertex plus |Kr| along psiElt; KrElt is stored as −|R|.
• Across a grating the path difference is defined modulo λ: compare wavefronts in phase, never as unwrapped lengths.
Reference document: optical_design/SPECTROMETER_DESIGN_REFERENCE.md (forms, conditions, metrics, references).